## Slide 1: Contracts and monitoring for Vision-based Auto Landing
Febuary 2023

## Slide 2: Problem Statement
Find Perception Contracts that are sufficient for assuring safety of vision-based auto-landing system
Use Perception Contract for runtime monitoring
Progress in the past week
Implementation of scene and simulation setup in Gazebo
Basic pose estimation setup (currently with large error)
Next: Planning and landing control

## Slide 3: System Architecture
Gazebo Simulator
(camera)
Keypoint Detector
Image
Pose Estimator
Keypoint Pixels
Generate ILS Trajectory
Controller
Aircraft Dynamics
Relative
Position
Rotation
Reference Trajectory
Yaw rate
Pitch rate
Acceleration
Aircraft State
x
y
Aircraft Direction

## Slide 4: Setting Up Closed Loop Simulation
Fixed wing aircraft with Dubin’s aircraft dynamics
Simulating aircraft with camera flying over runway in gazebo
Keypoint detection based on marker color and ground truth information about keypoint locations
Planning to explore using U-Net [Ronneberger 2015] for keypoint detection
Pose estimation using Perspective-N-Point (PNP) algorithm from OpenCV

## Slide 5: Accuracy of Pose Estimation
The estimated position of aircraft is relatively accurate
The estimated position of aircraft fluctuates as the pose of aircraft change
The estimated orientation of aircraft is not accurate

## Slide 6: Discussion
We are working on improving the pose estimation errors
How to perform runtime monitoring without ground truth?
Next Step
  Closed the loop for the simulation

## Slide 7: How to assure safety of DNN-driven autonomous system?
DNN
Camera
Controller
Car
We propose a notion of contracts to assure safety of vision-based lane keeping and similar systems which are becoming standard

## Slide 8: Summary
A method for system-level safety certification based on Perception Contracts
A method for constructing particular types of piece-wise linear and decision trees for perception contracts
Applications to lane keeping and drone formation flight
Publications
  Verifying Controllers with Vision-based Perception Using Safe Approximate Abstractions. Hsieh, Li, Sun, Joshi, Misailovic, and Mitra. In Conference on Embedded Software (EMSOFT) 2022 and Special Issue of TCAD, Shanghai, 2022.
  Challenges in Rebooting Autonomy with Deep Learned Perception. Abraham, Mayne, Perez, Hsieh, Li, Oliveira, Yu, Sun, Mitra. Industry track paper Embedded Software (EMSOFT) 2022, Shanghai, 2022.
  Assuring safety of vision-based swarm formation control. Hsieh, Li, Koh, and Mitra, under review 2023.
  Perception Contracts for Safety of ML-Enabled Systems. Astorga, Hsieh, Madhusudan, Mitra, under review 2023.

## Slide 9: Insight 1: system specification is well-defined against ground truth states
Image
Environment.
lighting, weather, etc.
Perception. relative position
Control action.
steering angle, etc.
def control(heading, dist):
# Calculate controller output
delta = heading + arctan(K*dist, VEL)
if ...
elif ...
...
return steering
DNN
Camera
Controller
Car
State. position
Invariance on state: Track lane center

## Slide 10: Insight 2: low dimensional contract with state + perception combined
Control action.
steering angle, etc.
NN Perception h
Sensor s
Controller
Car
Approximation for Perception
(Camera & DNN)
def control(heading, dist):
# Calculate controller output
delta = heading + arctan(K*dist, VEL)
if ...
elif ...
...
return steering
State. position
Perception. relative position
Invariance on state: Track lane center
Perception is a state estimation task which are naturally formalized w.r.t ground truth state.
Bypass the challenges on formalization and high dimensional images

## Slide 11: Ground truth state and perceived values
State x = (x, y, θ)
Percept z = (d, ψ) Ideal estimation m*(x)
Plot on perception domain d and ψ

## Slide 12: EMSOFT 2022: Safe set-valued approximation around an estimate mean center
Estimate mean (purple) from linear regression on sampled perception output, given round truth
  Note estimate is not centered around m*(x) (biased)
A reasonable circle around the mean should preserve system invariance
Drawback: Unsafe percepts region leading to violation of invariance needs to encode controller and vehicle dynamics and solve constrained optimization.
Unsafe percepts in red region will lead to wrong control actions and in turn violate invariance.

## Slide 13: PLDI 2023 submission: Insight is to separate safe and unsafe perception outputs
More generally, synthesize a Boolean formula (binary classifier) to separate safe perception output (positive examples) from unsafe percepts (negative examples).
Constrained optimization is conceptually to find the nearest unsafe percepts for bounding circle shaped formulas.
Unsafe percepts in red region will lead to wrong control actions and in turn violate invariance.

## Slide 14: The problem of learning approximations of perception
Design the hypothesis space by choosing “simple” logic formulas.
E.g., syntax for decision tree on axis-aligned half-planes
b ::= d ≥ c | ψ ≥ c
φ ::= ite(b, φ, φ) | true | false
Exact learning: Learned formula φ must exclude all negative examples to preserve system invariance.
Maximality: Cover as many positive examples allowed in hypothesis space

## Slide 15: Illustration of the iterative algorithm
Learner
Teacher
Done
Iteration 1
Iteration 2
Iteration 3
d ≥ -0.05
ψ ≥ 0.08
ite(d ≥ -0.05, ψ ≥ 0.08, false)

## Slide 16: Iterative teacher learner framework
We instantiate this framework with an exact decision tree learner and use Gurobi as the teacher.
We defined the logic syntax to learn over octagonal constraints.

## Slide 17: Comparison on EMSOFT and PLDI
Learned region can be nonconvex as allowed in the syntax of logic formulas.
Learned region can be unbounded due to saturated control output

## Slide 18: Next steps
A general learning framework to find PCs
  Choose simple logic formula syntax
  Iterative learner-teacher architecture
  Maximal to include as many observed percept values as possible
New formalization to support controllers with states
  E.g., past perceived values for filtering or prediction
Next: Runtime assurance and control synthesis using PCs

## Slide 19
New Verse library for verification
19
Learning sensitivity from data
Reachability, composition,
fixpoints
Exploiting symmetries in dynamics
[CAV 21, TACAS 19]
Learning reachability functions [TACAS 22]
JSON file
transition structure extracted
+
Black-box physics simulator
Transition logic
Executable access to mode dynamics
map / scenario
controller code
Multi-agent interactions

## Slide 20
We are building the Verse library for code-level verification of autonomy
Python Code for describing agent’s decision logic
Instantiate multiple agents, maps to construct complex air-traffic scenarios
Plug-in reachability analysis DryVR [4], Flow*
Safety requirements written as Python assertions
Applied to drone control system [Lin Song’22]
Verification and Certification
Sayan Mitra
[4] DryVR: Data-driven verification and compositional reasoning for automotive systems, Fan, Qi, Mitra & Viswanathan, CAV 2017, Heidelberg, Germany, July 24-28, 2017.

## Slide 21
Reachability analysis explores all uncertainties
Port agents to new maps and scenarios with few lines of code
Analyze scenario with different sensors
Safety requirements written as Python assertions
Create and analyze scenarios with many agents
Ready for incremental verification and symmetry reduction
Plug-in different reachability analysis DryVR [4], Flow*
Next Steps
Several ongoing collaborations
Parallelization of reachability algorithms with Ray
Sayan Mitra